## Slide 1: CubeSat
Contents
1. What is CubeSat?
2. Standard functions
3. Features
Conclusion
with Jérôme Skoda

## Slide 2: What is CubeSat?
Used for space research
Lowcost: 50 to 100 k€
Modular design
Miniaturized:
  1U: 10×10×10 cm (1 liter)
  2U: 20×10×10 cm
  3U: 30×10×10 cm
More launch opportunities
Figure 1 : CubeSat Orbital Deployer
Figure 2: ESTCube-1
Notes: Speed – able to exploit parallelism, especially with data intensive applications

## Slide 3: Standard functionality
Attitude Determination and Control System (ADCS)
On-Board Computer (OBC)
Communication system
Power system
Payload
Figure 3: Interior of cubesat
Notes: Speed – able to exploit parallelism, especially with data intensive applications

## Slide 4: Features
On-Board Computer:
  Processor: Power efficient (ARM)
  OS: FreeRTOS
Programming language:
  C, C++, VHDL, Verilog
Communication system
  Data rate: 1 Mbit/s
  Protocol: AX.25 / FX.25
  Frequency band: 2,0GHz to 2,3GHz
Others technologies used:
  FPGA / PSCOC
Source: SpaceCube, X-CubeSat and IgoSat
Figure 4: X-CubeSat Design Overview

## Slide 5: Conclusion
CubeSats offer more opportunities to launch new technologies into space
Figure 5: CubeSat Deployer on the ISS

## Slide 6: Reference
“CubeSat: A new Generation of Picosatellite for Education and Industry Low-Cost Space Experimentation”, H Heidt, J Puig-Suari, A Moore, S Nakasuka, R Twiggs, 2000
“The cubesat approach to space access”, A Toorian, K Diaz, S Lee, 2008
Special thanks
Spacelab of IUT de Cachan