CubeSat
Contents
1. What is CubeSat?
2. On-Board Computer
3. Ground Station
Conclusion
with Soufiane BAGHOR and Jérôme Skoda

---
What is CubeSat?
What is CubeSat?
- Used for space research
- Lowcost: 50 to 100 k€
  - COTS hardware
- Modular design
- Miniaturized: 1U to 12U
  - 1U: 10×10×10 cm (1 liter)
- More launch opportunities
Figure 1 : CubeSat Orbital Deployer
Figure 2: ESTCube-1
[Speaker Notes: Speed – able to exploit parallelism, especially with data intensive applications]

---
Standard functionality
Standard functionality
- Attitude Determination and Control System (ADCS)
- On-Board Computer (OBC)
- Communication system
- Power system
- Payload
Figure 3: Interior of cubesat
[Speaker Notes: Speed – able to exploit parallelism, especially with data intensive applications]

---
Features
Features
On-Board Computer:
  - Processor: Power efficient (ARM)
  - OS: FreeRTOS
- Programming language:
  - C, C++, VHDL, Verilog
- Communication system
  - Data rate: 1 Mbit/s
  - Protocol: AX.25 / FX.25
  - Frequency band: 2,0GHz to 2,3GHz
- Others technologies used:
  - FPGA / PSCOC
Source: SpaceCube, X-CubeSat and IgoSat
Figure 4: X-CubeSat Design Overview

---
Conclusion
Conclusion
CubeSats offer more opportunities to launch new technologies into space
Figure 5: CubeSat Deployer on the ISS

---
Reference
Reference
- “CubeSat: A new Generation of Picosatellite for Education and Industry Low-Cost Space Experimentation”,
  H Heidt, J Puig-Suari, A Moore, S Nakasuka, R Twiggs, 2000
- “The cubesat approach to space access”,
  A Toorian, K Diaz, S Lee, 2008
Special thanks
Spacelab of IUT de Cachan