## Slide 1
Contents
1. What is CubeSat?
2. On-Board Computer
3. Ground station
Conclusion
CubeSat
By
Soufiane BAGHOR <baghorsoufiane@gmail.com>
Jérôme SKODA <contact@jeromeskoda.fr>
Notes: 1

## Slide 2
1kg
50kg
200kg
800kg
0kg
Pico
PocketQube
0,5 Kg
Nano
EyeSat
4 Kg
Micro
Demeter
130 Kg
Mini
Corot
630 Kg
Pleiades
1 000 Kg
What is CubeSat?
CubeSat by Soufiane BAGHOR and Jérôme SKODA
20/11/2017
2

## Slide 3
What is CubeSat?
For space research
Miniaturized
  Simple 1U: 10×10× 10 cm
  Double 2U: 10×10× 20 cm
  Triple 3U: 10×10× 30 cm
  Etc 12U: 10×10× 120 cm
Lowcost
  Rapid development
  Modular design
  COTS hardware
CubeSat by Soufiane BAGHOR and Jérôme SKODA
20/11/2017
3
Figure 1: XcubeSat (Polytechnique)
SpaceCube (Mines)
Notes: Speed – able to exploit parallelism, especially with data intensive applications
3

## Slide 4
What is CubeSat?
Composition:
Attitude Determination and Control system (ADCS)
On-Board Computer
Communication system
Power system
Payload
Figure 2: Interior (QB50 precursor)
CubeSat by Soufiane BAGHOR and Jérôme SKODA
20/11/2017
4
Notes: Speed – able to exploit parallelism, especially with data intensive applications
4

## Slide 5
Controls all subsystems
Power efficient Microcontroller
  STM32 family chips
  ARM cortex M4/M7 processor
Language: C/C++
FreeRTOS
  Taskscheduling
  Semaphore
  Queue operations
Use Finite-state machine
  Good for debug, test and validation
On-Board Computer
Figure 3: System Block Diagram
Figure 4: State Transition Diagram
CubeSat by Soufiane BAGHOR and Jérôme SKODA
20/11/2017
5

## Slide 6
Figure 5: Single event upset
Autonomous system
Power efficient software coding
  No unnecessary action in background
  Handling Sleep Transitions Seamlessly
  Scale Behavior Based on Machine Power State
Space contraints
  Phantom Commands (PC)
  Random Part Failures (RPF)
  Single event upset (SEU)
On-Board Computer
CubeSat by Soufiane BAGHOR and Jérôme SKODA
20/11/2017
6

## Slide 7
Send Telecommand
Receive telemetry (Whole Orbit Data)
Language: Java
Antenna Tracking
  Change elevation and azimuth position
  Increased or reducing the frequency (Doppler shift)
Ground station
Figure 7:
Antenna UHF/VHF
(Ecole Polytechnique)
Figure 6 :
Antenna bande X
(CNES Toulouse)
CubeSat by Soufiane BAGHOR and Jérôme SKODA
20/11/2017
7

## Slide 8
Control command centers
  Attitude handling
Ground station
Figure 8: Satellite tracking (Gpredict)
CubeSat by Soufiane BAGHOR and Jérôme SKODA
20/11/2017
8
Satellite tracking
  Orbit determination

## Slide 9
CubeSats facilitate access to space and offer more opportunities to innovation
Figure 9: PlanetLabs CubeSat Constellation
CubeSat by Soufiane BAGHOR and Jérôme SKODA
20/11/2017
9
Conclusion

## Slide 10
CubeSat by Soufiane BAGHOR and Jérôme SKODA
20/11/2017
10
References
«CubeSat: A new Generation of Picosatellite for Education and Industry Low-Cost Space Experimentation», H Heidt, J Puig-Suari, A Moore, S Nakasuka, R Twiggs, 2000
«The cubesatapproach to space access», A Toorian, K Diaz, S Lee, 2008
«Design and Qualification of On-Board Computer for Aalto-1 CubeSat »ElyasRazzaghi, 2012
« CubeSatsgetbig», www.thespacereview.com. 2012.
« Small Spacecraft Technology State of the Art », NASA 2015
« Satellite communication», Henning Vangli2010
Image
2nd Workshop CubeSat (2017)
Special thanks
Spacelab of IUT de Cachan

## Slide 11
Thanks for your keen interest!
Any questions?
Contact
Soufiane BAGHOR <baghorsoufiane@gmail.com>
Jérôme SKODA <contact@jeromeskoda.fr>
Notes: 11